DR5810 & DR5810S Series Firmware Upgrade Guidelines  (V1.0.4)

Install Upgrading Tool software

Run “HRC7000_DMR_FACTORY_DL_TOOLS_V1.01.01_Setup.exe” to install.

Upgrade software

- As there are two kinds of hardware version (Different RED/FCC/IC ID), the different firmware version should be used. You could use the following way to know which hardware version of the radio and choose the corresponding firmware version.

|  | DR5810 Series | DR5810S Series | Remark |
| --- | --- | --- | --- |
| Serial Number | Digital (5&6) < D5 | Digital (5&6) >= D5 | e.g. 2405D555420301 (S version) |
| Hardware Difference | AK2365 + AK1590 | BK4819 |  |
| Hardware version | < V2.0 | >= V2.0 |  |
| Firmware version | V2.0x.xx | >= V3.0x.xx |  |
| PCB Top Layer |  |  |  |
| PCB Bottom Layer |  |  |  |
| FCC ID | Y4GDR5810-2 or -1 | Y4GDR5810S-2 or -1 |  |

- Press the TOP Key & PTT then power on the radio to enter the upgrading mode, the LED will show RED/GREEN/ORANGE circularly.

3)  Connect the programming cable with the computer.

4)  Run the “Factory Flash Tool” and then load the files needed to upgrade, i.e.V2.0x.xx or V3.0x.xx

.